## Slide 1: Dtect and Capillar: histological analysis tool
© 2019 Simon Holbeck. Validation and instructions by Roger Kissane.

## Slide 2: Table of contents
How to install and run? 3
Dtect 4 - 13
Capillar 14 - 19
Miscellaneous 20 - 26

## Slide 3: How to run Dtect?
Install MCRInstaller.exe
Download Dtect.exe and Capillary.exe and place into your desktop folder

## Slide 4: Dtect
Histological Fibre typing

## Slide 5: Generation of a digital skeleton
Open Dtect.
Click “load images”, and select the file type appropriate from the drop down menu (png, jpg, bmp or tiff).
Select the image you wish to digitize

## Slide 6: Save path
Click “Save Path” to select the folder you wish to save the generated matlab file and morphometric text data file
Click “OK” when selected desired folder

## Slide 7: Check the quality of the automatic lamina detection
Set pixels/mm.
Click “Watch Area” (selected blue). This will highlight fibres in magenta and number fibres that fit within the minimum and maximum threshold set. This allows visualization of regions that may need adding in or removing.

## Slide 8: Cleaning of basal lamina- noise thresholding
Set the noise threshold between 0 ~ 0.5 (will require some trial and error to see which factor removes the most noise without disturbing too much lamina).
Threshold = 0
Threshold = 0.1
Note: Thresholding will remove erroneous lamina, but too high a threshold may lead to removal of useful lamina boundaries.

## Slide 9: Cleaning of basal lamina- Deleting lamina
Select “Remove Lamina” (highlighted blue)
Click and hold down the mouse button while moving the curser through the region you wish to delete.
Release the mouse and it remove the segmented lamina
Note: if you accidently cross lamina that is wanted simply unselect “Remove Lamina” and click ”Undo”.

## Slide 10: Cleaning of basal lamina- Addition of missing lamina
Select “Draw Lamina”
To add lamina click along the lamina staining, using successive clicks to join smaller lamina segments together.
To finish the boundary double click at the end.
Note: When adding lamina you must cross two preexisting boundaries in order to create a new one

## Slide 11: Progress to fibre type allocation
Once you are happy with the skeleton of the click “Continue”.
Multiple options appear (Leeds1, Leeds2, LEeds3, AKI1, AKI2 and AKI3). trial and error which setting best automatically assigns your fibre type composition should be used.
Click “OK” and select which colour you have stained Type I fibres (using our protocol it will be RED)

## Slide 12: Redefining fibre type allocation
Having chosen the discriminator settings that best automatically assign fibre type, it may be that some are incorrectly assigned. To re-label:
Use the Fibre Traffic function to move fibres between the three windows. The selected toggle here will allow fibres to be moved between picture A and B.
Click on the fibre that you wish to move and it will appear in the corresponding box.
Note: Worth relabeling the pictures for their fibre types which are Type I, Type IIa and Type IIb/x

## Slide 13: Saving of data
When you are finished assigning fibre types to their correct window the data can be saved.
Click “Calculate Area” this will generate a text file with fibre composition and area.
The “Go To Export” button will become bold, click this button to call the Export window
Click “Export” to generate a matlab file that can be used in the Capillary.exe package

## Slide 14: Capillar
Association of capillaries with basal lamina

## Slide 15: Association of capillaries with muscle boundary skeleton
Open Capillary.exe.
Click “Import”, and select the Matlab file generated using Dtect.
Click “Open”.
This folder will be used as the save path for the capillary labelled matlab file

## Slide 16: Assign capillaries to boundary
Select “Mark”.
Click on the image where a capillary should be placed.
A yellow circle will appear with the centroid of the circle to be used as the point of oxygen supply later on in the oxygen transport modeler (OTM). The red numbers will increase incrementally within the fibre that the capillary is considered in contact with.
If a fibre number does not increase it could be because the marker size is not large enough, however the capillary can still be associated with the fibre by RIGHT clicking on the fibre you wish to assign the capillary to. You can then continue Left hand clicking and associating capillaries with each fibre.

## Slide 17: Identifying where to place capillaries
We have built in a number of functions to help identify the positions of capillaries. Mainly the removing of objects from the window:
Deselecting “Show Marks”, “Show lines” or ”Show Circles” will hide the various identifying shapes and numbers to clear the field of view.
Additionally you can just look at a single colour channel (Red or Green, depending on the capillary label used).

## Slide 18: Removing incorrectly placed capillaries
There are two ways to delete capillaries:
Immediately stop labelling
  Deselect “Mark”.
  Click “Delete Selected” and then reselect “Mark” to continue labelling.
Wait until you have labelled all capillaries
  Deselect “Mark”.
  Click “identifi cap”, click on the capillary to be removed.
  Click “Delete cap” and this will remove the identified capillary.

## Slide 19: Save capillary labelled files
Click “Save data and text”
NOTE: check the path folder that both a text file and matlab file have been generated with a filename ending with ‘_CAP’. This file you will use in the oxygen transport modeler (OTM).

## Slide 20: Miscellaneous
Window Orientation

## Slide 21: Screen Orientation – Dtect main screen
Minimum size of object
Zoom function (single click to zoom, or select zoom area. Double click to zoom out)
Noise thresholding to remove irregular detected lamina (0.1-0.4 works well)
Scaling factor in pixels per milimeter
Minimum area of a fibre – Dtect will not identify a fibre that is bellow this size
Maximum area of a fibre - Dtect will not identify a fibre that is above this size
Lamina membrane thickness, drop down menu of incremental lamina thicknesses
Remove lamina function (used to delete noisy/incorrectly placed lamina, simply click and drag cursor through lamina that is to be deleted)
Add missing lamina (to add boundaries click to begin the drawing tool. Each click will joint to the previous point, and double clicking will complete the drawing. To draw you must begin by crossing through pre-existing lamina boundaries, and finish crossing a boundary)
Undo button removes the last ‘draw’ or ‘remove’ function performed
Watch area button will show only the blue channel (for lamina boundaries) and the overlaid skeleton in red
Will present the original histology image without boundary overlay (for cross-checking where staining is variable)
Applies a region of interest to the image (only to be used if the capillary function is not to be used)
Views the placement of region of interest
Load button to import histology image (.png, .jpg, .bmp and .tif)
Save path to select folder for Matlab generated file to be saved in
Continue button to progress to fibre type allocation step
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 22: Screen Orientation – Fibre type allocation
1
2
3
4
5
1’
2’
3’
6
7
Type I fibre viewing window*
1’) Labelling of fibre type in the above window*
Type IIa fibre viewing window
2’) Labelling of fibre type in the above window
Type IIb/x fibre viewing window
3’) Labelling of fibre type in the above window
Muting window
Direction of fibre switching
Calculate area (.txt file)
7) Go To Export (opens new window to generate .mat file)
* if cardiac tissue is being processed position all fibres into the Type I window

## Slide 23: Screen Orientation – Capillar main screen
1
2
3
4
5
6
7
3’
8
9
10
11
12
13
14
15
Zoom function (single click to zoom, or select zoom area. Double click to zoom out)
Sets capillary marker size
Allows viewing of only green channel (for capillaries labelled in green)
3’) Allows viewing of only red channel (for capillaries labelled in red)
Toggles the visualisation of fibre numbers
Toggles the view of the magenta fibre boundary
Toggles view of capillary markers (yellow circles)
Select the mark function to add capillaries to the muscle fibre skeleton
Toggles the muted fibres on and off
A running count of the number of capillaries placed on the image
Identifies any selected capillary (clicked on any capillary while using this function will show all allocated fibres to that capillary, and allows for addition/removal of fibres)
Deletes the highlighted capillary and any association with suprounding fibres
Allows the editing of the region of interest to the image
Views the placement of region of interest
Import button to select the Matlab file generated in the Main Dtect program
Following completion of capillary allocation, clicking save data and text will generate a new Matlab file (with fibre boundary information and capillary position) and a text file (with raw capillary/fibre information)*
* be sure to check that a Matlab file has been generated in the designated folder before closing the window. The file name will have _CAP added to the end of the file name

## Slide 24: How to zoom
There are two ways to zoom in Dtect and Capillary, Select “Zoom”:
  A single on a region you are interested in will zoom in an preset magnification, which you can increase multiple times
  You can also click, hold down and drag a rectangle region to zoom in on
To zoom out double click on the image

## Slide 25: Setting the Region of Interest (ROI)
Dtect/Capillary.exe will assume the whole image as the region of interest, unless user defined.
Under ROI Settings, click “Edit”.
Drag a rectangle ROI over the image.
Letting go of the rectangle, Dtect will ask if you are happy with the placement, which can be re-done, cancelled completely, or continued and used.
You can edit this in both Dtect and Capillar.
Note: This is only worth doing if you are only interested in global fibre type and capillary indices, otherwise, do not use the ROI setting in Dtect, as this will be added during the oxygen transport modelling (OTM).

## Slide 26: Muting of fibres
Occasionally there may be tears in tissue, or fibres that you are unable to confidently assign a fibre type to, and want to remove from subsequent analysis
Clicking on the fibre in the bottom right hand window will turn the selected fibre grey across all of the windows. This ‘Mutes’ the fibre from analysis. It can be ‘unmuted’ by clicking the fibre again.